## Slide 1: The String Instructions
Reference: Assembly Language Programming and Organization of the IBM PC – Charles Marut – Chapter 11

## Slide 2: Overview
A memory string or string is an array of bytes or words.
We will see instructions to:
    Copy a string into another string
    Search a string for a particular byte or word
    Store characters in a string
    Compare strings of characters alphabetically

## Slide 3: The Direction Flag
The direction flag (DF) is a control flag. The control flags are used to control the processor’s operations.
The direction flag (DF) determines the direction in which string operations will proceed.
These operation are implemented using two index registers: SI and DI.

## Slide 4: The Direction Flag
String1 db ‘abcd$’
Offset ASCII character
  0200h a
  0201h b
  0202h c
If DF=0, SI and DI proceed in the direction of increasing memory addresses from left to right across the string. Conversely, if DF=1, SI and DI will proceed in the direction of decreasing memory addresses from right to left.

## Slide 5: CLD and STD
To make DF=0, use the CLD instruction
CLD ; clear direction flag
To make DF=1, use the STD instruction
STD ; set direction flag

## Slide 6: Moving a String
MOVSB
Copies the contents of the byte addressed by DS:SI to the byte addressed by ES:DI. The contents of the source byte are unchanged.
After the byte has been moved, both SI and DI are automatically incremented if DF=0, or decremented if DF=1.
Permits memory to memory operation

## Slide 7: Moving a String
.Data
String1 DB ‘HELLO$’
String2 DB 5 dup (?)
.Code
MOV AX, @Data
MOV DS, AX
MOV ES, AX
LEA SI, String1
LEA DI, String2
CLD
MOVSB ; String2
MOVSB ; String2
Before MOVSB |  |  |  |  | 
 | SI |  |  |  | 
String1 | ‘H’ | ‘E’ | ‘L’ | ‘L’ | ‘O’
 | DI |  |  |  | 
String2 |  |  |  |  | 
After MOVSB |  |  |  |  | 
 |  | SI |  |  | 
String1 | ‘H’ | ‘E’ | ‘L’ | ‘L’ | ‘O’
 |  | DI |  |  | 
String2 | ‘H’ |  |  |  | 

## Slide 8: The REP Prefix
MOVSB moves only a single byte from the source string to the destination string. To move the entire string, first initialize CX to the number N of bytes in the source string and execute
REP MOVSB
The REP prefix causes MOVSB to be executed N times. After each MOVSB, CX is decremented until it becomes 0.

## Slide 9: The REP Prefix
To copy string1 to string2 we execute:
  CLD
  LEA SI, String1
  LEA DI, String2
  MOV CX,6 ; Number of characters in String1
  REP MOVSB

## Slide 10: Moving a String
MOVSW ; word form of MOVSB
Copies the contents of the word addressed by DS:SI to the word addressed by ES:DI. The contents of the source word are unchanged.
After the word has been moved, both SI and DI are automatically incremented by 2 if DF=0, or decremented by 2 if DF=1.

## Slide 11: Store String
STOSB ; store string byte
Moves the contents of AL register to the byte addressed by ES:DI. DI is incremented if DF=0 or decremented if DF=1.
STOSW ; store string word
Moves the contents of AX register to the word addressed by ES:DI. DI is incremented by 2 if DF=0 or decremented if DF=1.

## Slide 12: Store String
MOV AX, @Data
MOV ES, AX
LEA DI, string1
CLD
MOV AL, ‘A’
STOSB
STOSB
Before STOSB |  |  |  |  | 
 | Di |  |  |  | 
String1 | ‘H’ | ‘E’ | ‘L’ | ‘L’ | ‘O’
After STOSB |  |  |  |  | 
 |  | Di |  |  | 
String1 | ‘A’ | ‘E’ | ‘L’ | ‘L’ | ‘O’
After Second STOSB |  |  |  |  | 
 |  |  | Di |  | 
String1 | ‘A’ | ‘A’ | ‘L’ | ‘L’ | ‘O’

## Slide 13: Load String
LODSB ; load string byte
Moves the byte addressed by DS:SI into AL. SI is incremented if DF=0 or decremented if DF=1.
LODSW ; load string word
Moves the word addressed by DS:SI into AX. SI is increased by 2 if DF=0 or decreased by 2 if DF=1.

## Slide 14: Load String
.Data
  String1 DB ‘ABC$’
.Code
  MOV AX, @Data
  MOV DS, AX
  LEA SI, String1
  CLD
  LODSB
  LODSB
Before LODSB |  |  |  |  | 
 | SI |  |  |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | 
After LODOSB |  |  |  |  | 
 |  | SI |  |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | AL=‘A’
After Second LODSB |  |  |  |  | 
 |  |  | SI |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | AL=‘B’

## Slide 15: Scan String
SCASB ; scan string byte
Can be used to examine a string for a target byte. The target byte is contained in AL.
SCASB subtracts the string byte pointed to by ES:DI from the contents of AL and uses the result to set the flags.
DI is incremented if DF=0 or decremented if DF=1.
SCASW ; scan string word
The target word is in AX.

## Slide 16: Scan String
.Data
  String1 DB ‘ABC$’
MOV AX, @Data
MOV ES, AX
LEA DI, String1
CLD
MOV AL, ‘B’
SCASB
SCASB
Before SCASB |  |  |  |  |  |  | 
 | Di |  |  |  |  |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | AL=‘B’ |  | 
After SCASB |  |  |  |  |  |  | 
 |  | DI |  |  |  |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | AL=‘B’ |  | ZF=0
After Second SCASB |  |  |  |  |  |  | 
 |  |  | DI |  |  |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | AL=‘B’ |  | ZF=1

## Slide 17: Scan String
If CX is initialized to the number of bytes in the string
REPNE SCASB ; Repeat SCASB while not equal to target
Repeatedly subtract each string byte from AL, update DI and decrements CX until the target is found or CX=0.

## Slide 18: Compare String
CMPSB ; compare string bytes
Subtracts the byte with address ES:DI from the byte with address DS:SI and sets the flags. Then both SI and DI are incremented or decremented depending on DF.
CMPSW ; compare string words

## Slide 19: Compare String
.Data
String1 DB ‘ACD$’
String2 DB ‘ABC’
.Code
MOV AX, @Data
MOV DS, Ax
MOV ES, Ax
LEA SI, String1
LEA DI, String2
CLD
CMPSB
CMPSB
Before CMPSB |  |  |  |  | 
 | SI |  |  |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | 
 | DI |  |  |  | 
String2 | ‘A’ | ‘C’ | ‘D’ |  | 
After CMPSB |  |  |  |  | 
 |  | SI |  |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | 
 |  | DI |  |  | ZF=1
String2 | ‘A’ | ‘C’ | ‘D’ |  | 
After CMPSB |  |  |  |  | 
 |  |  | SI |  | 
String1 | ‘A’ | ‘B’ | ‘C’ |  | 
 |  |  | DI |  | ZF=0
String2 | ‘A’ | ‘C’ | ‘D’ |  | 

## Slide 20
Thanks…….