## Slide 1
Branching Structure
Reference: Assembly Language Programming and Organization of the IBM PC – Charles Marut – Chapter 6

## Slide 2: Branching Structure
Branching structure enables a program to take different paths, depending on conditions.
Three types of branching structures:
● IF-THEN
● IF-THRN-ELSE
● Case
1

## Slide 3: Branching Structure: IF-THEN
Pseudocode in HLL:
IF condition is true
THEN
execute true-branch statements
End_if
condition
True branch
statements
false
true
2

## Slide 4: Example
Replace the number in AX by its absolute value.
Pseudocode Code
IF AX <0 CMP AX,0
Then JNL END_IF
replace AX by –AX NEG AX
END_IF END_IF:
3

## Slide 5: Branching Structure: IF-THEN-ELSE
Pseudocode in HLL:
IF condition is true
THEN
execute true-branch statements
ELSE
execute false-branch statements
End_IF
CONDITION
TRUE BRANCH
STATEMENTS
FALSE BRANCH
STATEMENTS
TRUE
FALSE
4

## Slide 6: EXAMPLE
Suppose AL and BL contains extended ASCII characters. Display the one that comes first in the character sequence.
Pseudocode Code:
IF AL < BL MOV AH,2 ; prepare to display
THEN CMP AL,BL ; AL<=BL?
display the char in AL JNBE ELSE_ ;no, display char in BL
ELSE MOV DL,AL ; move char to be displayed
display the char in BL JMP DISPLAY ; go to display
END_IF ELSE_: ; BL<AL
MOV DL,BL
DISPLAY:
INT 21H ; display it
END_IF:
5

## Slide 7: Branching Structure: CASE
A case is a multiway branch structure that tests a register, variable, or expression for particular values or range of values. The general form is as follows:
Case Expression
values_1: statements_1
values_2: statements_2
…………..
values_n: statements_n
END_CASE
6

## Slide 8
Case Expression:
values_1: statements_1
values_2: statements_2
…………..
values_n: statements_n
END_CASE
STATEMENTS_2
STATEMENTS_N
VALUE_1
VALUE_2
VALUE_N
…….
STATEMENTS_1
EXPRESSION
7

## Slide 9: EXAMPLE
IF AX contains a negative number, put -1 in BX; if AX contains 0, put 0 in BX; if AX contains a positive number, put 1 in BX.
8

## Slide 10
Pseudocode
Case AX
< 0:put -1 in BX
= 0:put 0 in BX
> 0:put 1 in BX
END_CASE
Code:
CMP AX,0 ; test AX
JL NEG ; AX<0
JE ZERO ;AX=0
JG POS ;AX>0
NEG: MOV BX,-1 ; put -1 in BX
JMP END_CASE ; and exit
ZERO: MOV BX,0 ; put 0 in BX
JMP END_CASE ; and exit
POS: MOV BX,1 ; put -1 in BX
END_CASE:
NOTE : only one CMP is needed, because jump instructions do not affect the flags.
9

## Slide 11: Branches with compound conditions
Sometimes the branching condition in an IF or CASE takes the forms
Condition_1 and condition_2
Condition_1 or condition_2
10

## Slide 12: AND conditions
An AND condition is true if and only if condition_1 and condition_2 are both true.
If any condition is false, then the whole thing is false.
Con1 & Con2
DISPLAY
false
true
EXIT
11

## Slide 13
Read a character and if it’s an uppercase letter, display it.
Pseudocode
If (‘A’ >= character) and (character <=‘Z’)
Then
Display character
End_if
EXAMPLE
Code:
MOV AH,1
INT 21H
CMP AL,’A’
JL END_IF
CMP AL,’Z’
JG END_IF
MOV DL,AL
MOV AH,2
INT 21H
END_IF:
12

## Slide 14: OR conditions
If condition_1 OR condition_2 is true then an OR conditions is true.
if both conditions are false, then the whole thing is false.
Con1 OR Con2
DISPLAY
false
true
EXIT
13

## Slide 15: Example
Read a character. If it’s “y” or “Y”, display it; otherwise, terminate the program.
Pseudocode
if (character = “y” or character= “Y”)
Then
Display character
Else
Terminate the program
End_if
Code:
MOV AH,1
INT 21H
CMP AL, ’y’
JE THEN
CMP AL,’Y’
JE THEN
JMP ELSE_
THEN:
MOV AH,2
MOV DL,AL
INT 21H
JMP END_IF
ELSE_:
END_IF:
14

## Slide 16: THANK YOU