## Slide 1: The Stack and Introduction to procedures
Reference: Assembly Language Programming and Organization of the IBM PC – Charles Marut – Chapter 8

## Slide 2: The Stack
A stack is a one dimensional data structure.
Items are added and removed from one end of the structure in a last in first out manner.
The most recent addition to the stack is called the top of the stack.
Stack instructions are PUSH, PUSHF, POP and POPF.
There is no effect of stack instructions on flags.

## Slide 3: Stack Instructions
PUSH source
Source is a 16 bit register or memory word.
PUSH AL > Illegal
.
.
.
00F0
00F2
00F4
0100
SP
AX=1234
SP=0100

## Slide 4: Stack Instructions
PUSH AX
SP is decreased by 2
A copy of the source content is moved to the address specified by SS:SP. The source is unchanged.
.
.
1234
00F0
00F2
00F4
0100
SP
AX=1234
SP=0100
00FE
Initially SP contains the offset address of the
memory location immediately following
the stack segment
The stack grows towards the
beginning of the memory
SP=00FE

## Slide 5: Stack Instructions
PUSHF
Pushes the contents of the flag register onto the stack.
POP destination
Destination is a 16 bit register (except IP) or memory word.

## Slide 6: Stack Instructions
POP BX
The content of SS:SP (top of the stack) is moved to the destination
SP is increased by 2
.
.
1234
00F0
00F2
00F4
0100
SP
00FE
BX=FFFF
SP=00FE
BX=1234
.
.
SP=0100
POPF pops the top of the stack into the flags register.

## Slide 7: Procedures
name PROC type
  ;body of the procedure
  RET
  name ENDP
Type (near or far) is optional
Near: the statement that calls the procedure is in the same segment as the procedure itself.
Far: the statement that calls the procedure is in a different segment.

## Slide 8: Procedures
The RET instruction causes control to transfer back to the calling procedure.
Every procedure should have a RET someplace.
Usually it is the last statement in the procedure.

## Slide 9: CALL and RET
To invoke a procedure, the CALL instruction is used.
There are two kinds of procedure calls, direct and indirect.
CALL name (direct)
CALL address expression (indirect)
Address expression specifies a register or memory location containing the address of a procedure.

## Slide 10: Executing a CALL Instruction
The return address of the calling program is saved on the stack. This is the offset of the next instruction after the CALL statement.
IP gets the offset address of the first instruction of the procedure. This transfers control to the procedure.

## Slide 11: Before CALL
OFFSET Address | Instruction
 | MAIN PROC
0010H | CALL PROC1
0012H | NEXT INSTRUCTION
 | ……….
 | PROC PROC
0200H | FIRST INSTRUCTION
0300H | RET
OFFSET Address | Instruction
00FCH | 
00FEH | 
0100H | 
CODE SEGMENT
STACK SEGMENT
IP
SP

## Slide 12: AFTER CALL
OFFSET Address | Instruction
 | MAIN PROC
0010H | CALL PROC1
0012H | NEXT INSTRUCTION
 | ……….
 | PROC PROC
0200H | FIRST INSTRUCTION
0300H | RET
OFFSET Address | Instruction
00FCH | 
00FEH | 0012
0100H | 
CODE SEGMENT
STACK SEGMENT
IP
SP

## Slide 13: Executing a RET Instruction
RET pop value
The integer argument pop value is optional.
For a NEAR procedure, execution of RET causes the stack to be popped into IP.
If a pop value N is specified, it is added to SP and thus has the effect of removing N additional bytes from the stack.
CS:IP now contains the segment:offset of the return address and control returns to the calling program.

## Slide 14: BEFORE RET
OFFSET Address | Instruction
 | MAIN PROC
0010H | CALL PROC1
0012H | NEXT INSTRUCTION
 | ……….
 | PROC PROC
0200H | FIRST INSTRUCTION
0300H | RET
OFFSET Address | Instruction
00FCH | 
00FEH | 0012
0100H | 
CODE SEGMENT
STACK SEGMENT
IP
SP

## Slide 15: AFTER RET
OFFSET Address | Instruction
 | MAIN PROC
0010H | CALL PROC1
0012H | NEXT INSTRUCTION
 | ……….
 | PROC PROC
0200H | FIRST INSTRUCTION
0300H | RET
OFFSET Address | Instruction
00FCH | 
00FEH | 
0100H | 
CODE SEGMENT
STACK SEGMENT
IP
SP

## Slide 16: Example: Write an assembly code that will count the number of 1’s in the content of AX register.
MOV AX,3H ; Value to be counted
CALL PROC1
HLT
PROC1 PROC
MOV BX, 0 ; Initialize Counter
START: CMP AX, 0 ; Check for ending
JZ END
TEST AX, 1 ; Check for 1
JZ BELOW
INC BX ; Increment count
BELOW: SHR AX, 1
JMP START
END: RET
PROC1 ENDP

## Slide 17
Thanks…….